2012/12/29 DAC.

Organizational notes:

1. All of the images and results are for the original subjects in the RIDER
   Pilot (NBIA) and Coffee Break (MSKCC) (TCIA) collections and use the same
   Patient's Name and Patient's ID values as the images from those
   collections
   
2. Results are described in DICOM SR files, which in turn reference DICOM
   segmentation files that encode the region as a 3D raster, and presentation
   states that record the zoom, pan and window levels at the time of measurement
   
3. Each timepoint involved measuring a single nodule (a "subject"), though the
   same image dataset may contain multiple nodules and have been reused multiple
   times.
   
4. There is one SR file per pair of timepoints per reader per nodule measured.

   In all the SR files, the (112039,DCM,"Tracking Identifier") references the,
   the specific case#, e.g., case# 57
   
   The (112040,DCM,"Tracking Unique Identifier") is shared for the different
   scan# measurements of the same case#.
   
   The (RP-100009,99RPH,"Worklist Sub-task Name") describes which nodule (case#) 
   was measured and the order of the time points (scan#) in the form:
   
     "case#-scan#-case#-scan#-firstOrSecondTimepointReadThisSubTask"
   
   where case# and scan# are those defined in the spreadsheets that listed the
   lesions for the experiment:
   
        UCLA_CoffeeBreak_lesion_detailsv3-1_26Aug2009.xls
        QIBA_1B_clinical_workflow_change_lesions_v2.xls
	
   e.g., "57-2-57-1-A" or "57-2-57-1-B" describe that case# 57 scan# 2 was
   read in the first sub-task, then case# 57 scan# 1 was read next (i.e., for
   this example, the reverse order to that in which they were acquired)
   
   Within each set of timepoint-specific results in the cummulative SR file,
   the (RP-100018,99RPH,"Subject Time Point Unique Identifier") is of the form:
   
     "subtask#-session#-timepoint#"

   where subtask# corresponds to the row of the experimental design (randomization)
   spreadsheet (with the first row for a session numbered from 0), session# is
   the Session ID value for the column, and timepoint# is 0 for the 1st timepoint
   (series read) and 1 for the 2nd timepoint (Series read); note that the
   timepoint# is NOT the scan#
   
   e.g., "11-9-0" then "11-9-1" describes that the 12th row of the randomization
   spreadsheet for the 9th session (reader 3 day 3) were read. For this
   experiment, timepoint# 0 and 1 will always be encoded in the cummulative
   SR file in that order, and these results for sub-task "57-2-57-1-B",
   indicate that the "11-9-0" time point results correspond to case#57 scan#2,
   and those for the "11-9-1" correspond to case#57 scan#1.
   
   Also, timepoint# is also encoded in (or more precisely, happens to be the
   same as) (RP-100553,99RPH,"Time Point Order").

5. Readers are identified by number (from 1 through 5) in the SR content item
   (RP-100007,99RPH,"Identifier within Person Observer's Role"), and their actual
   identity recorded in the SR tree in observer context and worklist descriptions
   has been removed. There is overlap of 4 of the 5 readers with the 1B Round 1
   experiment as follows:
   
    Round 2 reader    was Round 1 reader
        1                   3
        2                   4
        3                   na.
        4                   1
        5                   2

6. The SR files are in separate DICOM studies, dated as per the date of the most
   recent time point read (not the date that the read was performed) since the
   reading software used is designed to allow reading multiple time points
   (studies on different dates) and store all time point information for one
   reader in one (cummulative) SR instance, and this collection there are indeed
   multiple time points per SR instance

7. The SEG and PS instances are in the same DICOM study as the images to which
   they apply, but in separate series

8. The segmentation files contain 8 bit (not single bit) values, with only values
   0 and 255 used; they are co-planar with the original image slices with a 1:1
   voxel correspondence (same in-plane pixel spacing and cross-plane reconstruction
   interval) but encode only a sub-region of the volume sufficient to enclose the
   lesion volume (i.e., the frame and in-plane origin are different than those
   in the original slices).

9. The actual series (acquisition) on which the segmentation was performed is not
   explicitly encoded in the segmentation instance itself, but can be determined
   either from the SR image references for the automatically derived SD and LD,
   or from the series referenced from the presentation state that is referenced
   in the IMAGE content item in the SR that references the segmentation, or from
   the commonality of the FrameOfReferenceUID value in the segmentation and CT
   images (which is different for each scan).

10. Also included are the SR and PS files that were used for each time point to
    designate the location of the lesions to the readers; these contain one
	annotation per time point, and the SRs are in Series 90002 with the same
	Study Date as the referenced images (as opposed to Series 001 for the
	actual results)