2011/12/01 DAC.

Organizational notes:

1. All of the images and results are for one subject (patient), QIBA_CT_1C,
   since they all apply to the same physical phantom instance
   
2. There is one series per reconstruction  for each CT acquisition (which in the
   case of Toshiba required splitting multiple acquisitions per series into
   separate series and assigning new Series Instance UIDs).

3. Results are described in DICOM SR files, which in turn reference DICOM
   segmentation files that encode the region as a 3D raster, and presentation
   states that record the zoom, pan and window levels at the time of measurement
   
4. There is one SR file per read; each read is of one lesion performed by one
   reader on one CT acquisition (series); the lesion is labeled "VOLUME" in
   every read but each has a different UID; the Worklist Sub-task Name (e.g.,
   "3V1D-1") can be used to establish the relationship to the experimental
   design (reader V lesion site - arm); the sites are encoded:
   
   "A","Toshiba"
   "B","FDA"
   "C","UMD"
   "D","NIST"
   "E","Duke"
   "F","UCLA"
   
   which will also be apparent from the Procedure Description (copied from Study
   Description in the images); the reader # is also present in Identifier within
   Person Observer's Role

5. Readers are identified by number and their actual identity recorded in the SR
   tree in observer context and worklist descriptions has been removed

6. The SR files are in separate DICOM studies, dated as per the date of the read,
   since the reading software used is designed to allow reading multiple time points
   (studies on different dates) and store all time point information for one
   reader in one (cummulative) SR instance, even though for this collection
   there is only one time point per instance

7. The SEG and PS instances are in the same DICOM study as the images to which
   they apply, but in separate series

8. The segmentation files contain 8 bit (not single bit) values, with only values
   0 and 255 used; they are co-planar with the original image slices with a 1:1
   voxel correspondence (same in-plane pixel spacing and cross-plane reconstruction
   interval) but encode only a sub-region of the volume sufficient to enclose the
   lesion volume

9. The actual series (acquisition) on which the segmentation was performed can be
   determined from the SR image references for the automatically derived SD and
   LD (since this is not explicitly encoded in the segmentation instance itself)


Known DICOM issues in results files:

1. Segmentation instances contain incorrect value for Segmentation Algorithm Type
   (0062,0008); is "SEMIAUTOMATED"; standard requires "SEMIAUTOMATIC"
   
2. SR segmentation method value for random walker has code value and coding scheme
   designator swapped; i.e., CODE: (122554,DCM,"Segmentation Method")  =
   (99RPH,RP-101030,"Random Walker 3D") should be CODE: (122554,DCM,
   "Segmentation Method")  = (RP-101030,99RPH,"Random Walker 3D")

3. In PS and SEG instances, Manufacturer etc. is copied from the CT images to
   which they apply, and is not set to the actual creator (SCR)

4. The SR files do not contain a list of SOP Instances referenced in the content
   tree in Current Requested Procedure Evidence Sequence (0040,A375) as required
   by the standard

5. The creation dates and times in the SEG and PS files are in local time and the
   timezone is not explicitly specified, unlike the SR files where the dates and
   times are in UTC

6. Negative values in numeric SR content items exceed the maximum allowable length
   for the DS VR (which is 16)