## Slide 1: Introduction to the QIBA Process and Metrology
Kevin O’Donnell
Chairman, QIBA Process Cmte
Sr. Mgr., R&D, Toshiba Medical Research Institute USA, Inc.

## Slide 2: Clinical Decisions from Quantitative Imaging
QIBA Profile
Treat
Wait
Measure = 7
±6
?
Problem
Analysis
Solution
Treat
Wait
±2
!
Goal
Measure = 7
±6
Sources of Variance
Differences in:
- Patient Handling
- Acq. Protocols
- Reconstruction
- Segmentation
. . .
When all participating actors conform…
Protocol Reqs
Recon Reqs
Resolution Reqs
Noise Reqs
Segment. Reqs
Patient Prep & Operation Reqs
Segment. Reqs
Calibration Reqs
Notes: Purpose: Use Quantitative Imaging Biomarkers to inform Clinical Decisions
QIBA’s mission is to improve the value and practicality of quantitative imaging biomarkers by reducing variability across devices, clinical sites and time.
What’s the problem? Variability: need to be repeatable, robust => Industrial
We expect to collaborate to achieve this.

## Slide 3: QIBA Process
Select a Biomarker
Academic Research
Clinical Trials
&
Clinical Practice
Publish Profile
Coordinate Groundwork
Draft Profile
Validate Equipment & Sites
Identify significant sources of variance
Estimate achievable repeatability and accuracy
Validate underlying assumptions and mechanisms
Determine details critical to specify in the Profile
Initiate regulatory engagement
Make Profile available to the community
Engage with sites/trials adopting the Profile
Converge practice; reduce gratuitous variation
Document the agreed parameters and procedures
Specify details necessary to be robust in general use
Drive out any impeding variance and complexity
Make details stable, clear, implementable, testable
Test conformance with QIBA Profile specifications
Publish validated products/sites
Apply selection criteria: Translational, Transformational, Practical, …
Draft Initial Performance Claim

## Slide 4: QIBA Biomarker Selection
Dr. Dan Sullivan, founding chairman of QIBA, proposed 5 characteristics:
  Translational — ready to move from research into clinical care
  Transformational – considerable impact on public health
  Feasible — good chance of success in a reasonable time frame
  Practical — cost-effectively use existing resources where possible
  Collaborative — existing interest across stakeholders
QIBAs job is not exploration; QIBAs job is industrialization
  Make a biomarker robust, reliable and available
  Bring it “the last mile” into clinicians hands where it can help patients
  Too few biomarkers reach that point
Notes: Very large number of biomarkers in research literature and many look wonderful.
QIBA is a partnership between researchers and hospital doctors and equipment manufacturers and government agencies to bring biomarkers the last mile into the hands of all doctors.
Doing this takes resources from everyone, so we need to pick the best, most promising.
After we deliver, we can select some more.

## Slide 5: QIBA Profile Structure
Claims:
“95% probability that measured change -25% to +30% encompasses the true tumor volume change…”
Requirements:
Actor Table
Acquisition Device
Measurement Software
Radiologist
Activity Definitions
Product Validation
Calibration / QA
Patient Preparation
Image Acquisition / Recon
Post-Processing
Analysis / Measurement
User View
Will it do what I need?
What/who do I need
involved?
What do I have to do
to achieve the Claims?
(requirement checklists: procedures, training, performance targets)
How will I be tested?
Vendor View
Why do you want me to do this?
Which of my products
are affected?
What do I have to implement;
(requirement checklists: features, capabilities, performance targets)
How will I be tested?
Assessment Procedures:
Image Noise and Resolution Tumor Volume Change Variability
Site Performance
Notes: The Claim states the Technical Performance the Profile provides for the Biomarker.
The Requirements describe what must be done to meet the Claims.
The Assessment Procedures describe what must be done to assess specific Requirements (as needed).
Note: Do not dictate or re-iterate medical practice, imaging charter, or how to run and IRB. That’s not QIBA’s job,

## Slide 6: QIBA Profile Stages
Stage Name | Stage Meaning | Stage Criteria
Public Comment | Key factors affecting the Claim are described and addressed. Committee of experts believe it practical and expect claimed performance will be achieved. | Actor requirements clear & justified Open issues clearly listed Some groundwork may be ongoing
Consensus | Wider review & consensus; ready for trial use. | Public Comments addressed Text reasonably stable Open issues mostly resolved
Technically Confirmed | Profile is practical to understand and use. | Procedures implemented at test site Text stable Open issues resolved
Claim Confirmed | Claimed performance can be achieved. | Performance measured at test site Profile Claims achieved
Clinically Confirmed | Claimed performance will typically be achieved. | Profile Claims achieved in clinical use at multiple sites Note: QIBA doesn’t currently evaluate or coordinate transition to this stage
Progressive levels of stability and confidence

## Slide 7: QIBA Profile Stages
Stage Name | Stage Meaning | Stage Criteria
Public Comment | Key factors affecting the Claim are described and addressed. Committee of experts believe it practical and expect claimed performance will be achieved. | Actor requirements clear & justified Open issues clearly listed Some groundwork may be ongoing
Consensus | Wider review & consensus; ready for trial use. | Public Comments addressed Text reasonably stable Open issues mostly resolved
Technically Confirmed | Profile is practical to understand and use. | Procedures implemented at test site Text stable Open issues resolved
Claim Confirmed | Claimed performance can be achieved. | Performance measured at test site Profile Claims achieved
Clinically Confirmed | Claimed performance will typically be achieved. | Profile Claims achieved in clinical use at multiple sites Note: QIBA doesn’t currently evaluate or coordinate transition to this stage
Progressive levels of stability and confidence

## Slide 8: QIBA Profile Stages
Stage Name | Stage Meaning | Stage Criteria
Public Comment | Key factors affecting the Claim are described and addressed. Committee of experts believe it practical and expect claimed performance will be achieved. | Actor requirements clear & justified Open issues clearly listed Some groundwork may be ongoing
Consensus | Wider review & consensus; ready for trial use. | Public Comments addressed Text reasonably stable Open issues mostly resolved
Technically Confirmed | Profile is practical to understand and use. | Procedures implemented at test site Text stable Open issues resolved
Claim Confirmed | Claimed performance can be achieved. | Performance measured at test site Profile Claims achieved
Clinically Confirmed | Claimed performance will typically be achieved. | Profile Claims achieved in clinical use at multiple sites Note: QIBA doesn’t currently evaluate or coordinate transition to this stage
Progressive levels of stability and confidence

## Slide 9: QIBA Profile Stages
Stage Name | Stage Meaning | Stage Criteria
Public Comment | Key factors affecting the Claim are described and addressed. Committee of experts believe it practical and expect claimed performance will be achieved. | Actor requirements clear & justified Open issues clearly listed Some groundwork may be ongoing
Consensus | Wider review & consensus; ready for trial use. | Public Comments addressed Text reasonably stable Open issues mostly resolved
Technically Confirmed | Profile is practical to understand and use. | Procedures implemented at test site Text stable Open issues resolved
Claim Confirmed | Claimed performance can be achieved. | Performance measured at test site Profile Claims achieved
Clinically Confirmed | Claimed performance will typically be achieved. | Profile Claims achieved in clinical use at multiple sites Note: QIBA doesn’t currently evaluate or coordinate transition to this stage
Progressive levels of stability and confidence

## Slide 11: QIBA Metrology Concepts
Nancy Obuchowski, PhD
Cleveland Clinic Foundation

## Slide 12: Repeatability vs. Reproducibility
Repeatability
observations in a short time on the same subject under the same conditions; “test-retest”
residual variability reflects subject positioning, image noise, etc.
Reproducibility
observations in a short time on the same subject, but the measuring system (facility, operator, and/or measuring device) may differ
 | Repeat-ability | Reproduc-ibility
Measurement procedure | same | same
Measuring device | same | same or different
Operator | same | same or different
Facility | same | same or different
Notes: Short time is part of factoring out biological change.

## Slide 13: 95% Confidence Interval (CI)
Interval where the true value lies with 95% confidence
  Gives a practical sense of performance
  E.g. measured SUVmax = 3.2, and the 95% CI = [ 2.9, 3.5 ]
  Reflects the estimated bias (interval center) and variability (interval width)
Example Usage: Estimated slope of line (β)
  95% CI for β = [-3.3, +5.0]
  Interval contains 1.0, but is wide and contains many values not near 1.0
  It would be wise to get more data!
Notes: Graphic

## Slide 14: Cross-sectional vs. Longitudinal
Cross-sectional Claim
Performance measuring a value (Y) at a single timepoint
  Tumor glycolytic activity (SUVmax) measurements have a within-subject coefficient of variation (wCV) of 10%. The 95% CI = Y ± (1.96 × Y × wCV)
Longitudinal Claim
Performance measuring change over multiple timepoints
  For a measured change in shear wave speed of (Y2-Y1), a 95% confidence interval for the true change is (Y2-Y1) ± 1.96 × [(Y1 × 0.05)2 + (Y2 × 0.05)2]1/2
Useful characteristic: if bias is consistent, it cancels out
Notes: Graphic

## Slide 15: QIBA Profile Claim Selection Flowchart
1. Type of Claim
2. Characterize Bias
Scenario A Constant wSD; negligible bias:
Construct 95% CI from
wSD
Scenario B Constant wSD; bias known:
Construct 95% CI from TDI and wSD
Scenario C Constant wCV; negligible bias:
Construct 95% CI from
wCV
Scenario D Constant wCV; bias known:
Construct 95% CI from TDI and wCV
Scenario E Multiple wCVs; negligible bias:
Construct 95% CIs in multiple claims from different wCVs
Scenario F Multiple wCVs; bias known:
Construct 95% CIs in multiple claims from different TDIs
X-sectional
1a. Same measuring system at all time-points?
Scenario G
Constant wSD:
Construct 95% CI from wSD & estimated RC
Yes
Longitudinal
Scenario H
Constant wCV:
Construct 95% CI from wCV & estimated RC
Scenario I
Multiple wCVs:
Construct 95% CIs in multiple claims from different wCVs & estimated RCs
No
Scenario J Constant wSD; negligible bias:
Construct 95% CI from wSD & estimated RDC
Scenario K Constant wCV; negligible bias:
Construct 95% CI from wCV & estimated RDC
Scenario L Multiple wCVs; Negligible bias:
Construct 95% CIs in multiple claims from different wCVs & estimated RDCs
Scenario M Constant wSD; bias known:
Construct 95% CI from TDI, wSD & estimated RDC
Scenario N Constant wCV; bias known:
Construct 95% CI from TDI, wCV & estimated RDC
Scenario O Multiple wCVs; bias known:
Construct 95% CIs in multiple claims from different TDIs & estimated RDCs
Negligible
3. Characterize wSD or wCV
Known
Unknown
Use Longitudinal Claim
2. Characterize Bias
Negligible
Known
Unknown
Common
Use same system
Constant wSD
Constant wCV
Multiple wCVs

## Slide 16: Claim Scope
Approaches to characteristics that degrade performance
  Head motion, small lesions, spiculated lesions
Control/compensate
  Profile requires head immobilizer or motion compensation
Separate claims for different subpopulations
  Claim 1: wCV=0.11 for 50mm lesions
  Claim 2: wCV=0.25 for 10mm lesions
Exclude subpopulation from claim
  Claim holds for non-spiculated lesions

## Slide 17: Conformance Testing Sample Size
If claim performance target is wSD=7 (Perc 15 Profile)
  For actors with an expected performance of wSD=4.0, demonstrating conformance to wSD <7 only needs ≈13 subjects
If claim performance target is wCV=8% (CT Volumetry Profile)
  For actors with expected wCV=5%, need ≈17 subjects
  For actors with expected wCV=6%, need ≈43 subjects
  For actors with expected wCV=7%, need ≈190 subjects
Be cautious about setting aggressive performance targets
Notes: Note: when using in a clinical trial, need to incorporate between-subject variability to plan sample size for trial.

## Slide 18: Reference Papers: Introduction to Metrology Series
Statistical Methods in Medical Research, May 2014:
The Emerging Science of Quantitative Imaging Biomarkers: Terminology and Definitions for Scientific Studies and Regulatory Submissions
Quantitative Imaging Biomarkers: A Review of Statistical Methods for Technical Performance Assessment
Quantitative Imaging Biomarkers: A Review of Statistical Methods for Computer Algorithm Comparisons
Statistical Issues in the Comparison of Quantitative Imaging Biomarker Algorithms using Pulmonary Nodule Volume as an Example
Meta-Analysis of the Technical Performance of an Imaging Procedure: Guidelines and Statistical Methodology