Study 3A: Inter-algorithm Performance Investigation Study Design

January 2012

Rev 1.0

Document Revisions:

| Revision | Revised By | Reason for Update | Date |
| --- | --- | --- | --- |
| 0.1 | Andrew Buckler | Initial version | March 21, 2011 |
| 0.2 | Dave Gustafson | Clarified scope of study | April 13, 2011 |
| 0.3 | Maria Athelogou | Continued to clarify scope | April 28, 2011 |
| 0.4 | Grace Kim | Updated definitions for performance | June 6, 2011 |
| 0.5 | Hubert Beaumont | Improved document organization | July 20, 2011 |
| 0.6 | Andrew Buckler | Added radar plots and compliance assessment | July 27, 2011 |
| 0.7 | Dave Gustafson | Specified algorithm types, etc. | August 11, 2011 |
| 0.8 | Maria Athelogou | Resolved inconsistencies | October 20, 2011 |
| 0.9 | Andrew Buckler | With GK and MA, resolved remaining markups | December 28, 2011 |
| 1.0 | Grace Kim | Fleshed out statistical analysis | January 17, 2012 |

Table of Contents

1. Introduction	3

1.1. Purpose & Scope	4

1.2. Definitions	4

1.2.1. Technical Performance of the Measure	5

2. General implementation of the challenge studies	6

2.1. Flow of events for each challenge study	6

2.2. Results	7

2.3. Study Design	8

2.3.1. Data	8

2.3.2. Location Coordinates and Ground Truth	8

2.3.3. Approach to Statistical Analysis of the Challenges	8

2.3.3.1. Characterizing Performance of Absolute Volume Estimation where Ground Truth is Known	9

3. Endpoints and Investigations	12

3.1. Primary Investigations	13

3.2. Secondary investigations (future plans, needs study design extension in the future)	13

3.3. Primary and secondary endpoints	14

3.3.1. First 3A challenge study: Absolute volume estimation	14

3.3.1.1. Statistical Analysis of First 3A Challenge	15

3.3.2. Present thought on next 3A challenge study	15

Appendix: Factor Effects Model- full details	16

References	26

# Introduction

X-ray computed tomography (CT) is often an effective imaging technique for assessing therapy response. In clinical practice, qualitative impressions based on nothing more than visual inspection of the images are frequently sufficient for making some clinical management decisions. Quantification becomes helpful when lesion masses change slowly over the course of illness. Many investigators have suggested that quantifying whole lesion volumes could solve many of the limitations of RECIST’s current dependence of uni-dimensional diameters on axial slices, and have a major impact on patient management., Studies have shown that volumetry has value, however, some reports about the precision,, and accuracy of measurement have led to concerns about the risks of confusing variability with medically meaningful changes.

QIBA has constructed a systematic "process map" to qualifying volumetry as a biomarker of response to treatments for a variety of medical conditions, including lung disease. Several trials are now underway to provide a head-to-head comparison between volumetry and RECIST in multi-site, multi-scanner-vendor settings. The QIBA Profile is expected to provide specifications that may be adopted by users as well as equipment developers to meet targeted levels of accuracy and clinical performance in identified settings, both as a correlation to clinical outcomes as well as a comparison to the accepted measure of uni-dimensional diameters.

One approach to encouraging innovation that has proven productive in many fields is for an organization to announce and administer a public “challenge” whereby a problem statement is given and solutions are solicited from interested parties that “compete” for how well they address the problem statement.  The development of image processing algorithms has benefitted from this approach with many organized activities from a number of groups.  Some of these groups are organized by industry (e.g., Medical Image Computing and Computer Assisted Intervention or MICCAI), academia (e.g., at Cornell University), or government agencies (e.g., NIST).  This workflow is intended to support such challenges.

It is important to note that one of the reasons for doing this 3A study is to meet the need that a biomarker is defined in part by the “class” of tests available for it.  That is, it is not defined by a single test or candidate implementation but rather by an aggregated understanding of the results of such tests.  As such, it is necessary through this or other means to organize activities to determine how the class performs, irrespective of any candidate that purports to be a member of the class.  The corresponding workflow is related to the “Compliance / Proficiency Testing of Candidate Implementations” workflow and it may be that an organization such as NIST can both host challenges as well as serve in the trusted broker role using common infrastructure for these separate but related functions.

In summary, 3A is motivated by the following:

- Changes in malignant nodule volume is important for diagnosis, therapy planning, therapy response evaluation

- Measuring volume changes requires high accuracy in measurement of absolute volume

- Volumes of synthetic nodules may be measured with high accuracy

- Therefore it make sense to use such phantom data (as ground truth) in order to calculate accuracy measurement of algorithms

- The study results could be combined with the QIBA 1A and 1B Group work. This combination will improve the QIBA volumetric CT Profile development.

We will proceed to add reference clinical data sets, e.g., from Volcano, LIDC and other studies, moving forward wherein at least volume change can be measured by these methods, even if ground truth is not available (e.g., no pathologic specimen to compare to)

## Purpose & Scope

The primary and first aim of the study is to estimate inter- and intra-method variability by the volume estimation of synthetic nodules from CT scans of an anthropomorphic phantom (according to the work of the QIBA 1A Group. An inter-algorithm study, in the same way QIBA has been working on inter-reader, inter-scanner, and inter-site.  We will also connect the output of this study to the analysis section of QIBA Profile.  The aim of the study is not a measure of which of several methods provides the best image analysis.  Rather, the aim of the study is to gain knowledge to improve QIBA Volumetric CT Profiles and to provide context in which multiple parties have incentives to participate, while avoiding competition and supporting cooperation with a conjoint approach.

Participants include academic and commercial algorithm developers.  Industrial vendors may include, for example possible vendors, according to the Volcano 2009 challenge could be: Siemens, Philips, MeVis, Kitware, Definiens, Intio, VIA CAD etc…)

Scope of the study includes the following types of approaches:

- An automatic segmentation algorithm does not require any user intervention (include detection).

- A semi- automatic method needs minimal amount of input from user, e.g., a seed point to initialize the segmentation, then

  - user allowed to edit

  - user does not edit

Description/Classification of the methods: according to the grade of user intervention is needed (for example Volcano’09, A. P. Reeves et al):

- Totally automatic using seed points (no editing beyond setting initial seed)

- Limited parameter adjustment (on less than 15% of the cases)

- Moderate parameter adjustment (on less than 50% of the cases)

- Extensive parameter adjustment (more than 50% of the cases)

- Limited image/boundary modification (on less than 15% of the cases)

- Moderate image/boundary modification (on less than 50% of the cases)

- Extensive image/boundary modification (more than 15% of the cases)

## Definitions

It should be noted that certain terms, notably precision, accuracy, repeatability, reproducibility, variability, and uncertainty, are examples of terms that represent qualitative concepts and thus should be used with care (http://physics.nist.gov/Pubs/guidelines/appd.1.html#d12).  For example, the accuracy should not be equated with small bias; the Wikipedia definition suggests that accuracy and precision are independent. Accuracy in our opinion should be defined in terms of bias and precision so that high accuracy implies a small bias and a high precision. The Wikipedia definition implies that high accuracy can occur with low precision.

In metrology, it is said that no measured value is complete without an indication as to its uncertainty.

- Uncertainty: A value, associated with the result of a measurement, that characterizes the dispersion of the values that could reasonably be attributed to the measurement, composed of uncertainty from both random and systematic error.  Random error contributes to reliability, whereas systematic error contributes to validity (http://www.ncbi.nlm.nih.gov/pmc/articles/PMC1250265).

This uncertainty may derive from the technical performance characteristics of the measure, and/or the applicability of the measure to the clinical context for use.  At root, these two contribute to the uncertainty.  It is generally understood that characterization of technical performance is undertaken as a foundation for clinical performance.  Once a measurement is characterized in terms of its ability to created results at known levels of bias and variance, it becomes defined to layer clinical performance on top of it.  It is an open question at this time whether the progression from technical to clinical performance is merely translating the uncertainty from one domain to the other using linear algebra or whether in some biomarkers a non-linear model is needed.

### Technical Performance of the Measure

- Bias: A quantitative term describing the difference between the average of measurements made on the same object and its true value. In particular, for a measurement laboratory, bias is the difference (generally unknown) between a laboratory's average value (over time) for a test item and the average that would be achieved by the reference laboratory if it undertook the same measurements on the same test item (http://www.itl.nist.gov/div898/handbook/mpc/section1/mpc113.htm).

Specifically: mean of measured volume minus the physical measurement of the anthropomorphic phantom object.  Expressed as fraction of actual.

where    is a measured value  in ith and jth object,  Y.. is a population mean, Y..  is a sample mean as an estimated of population mean from the sample, N (= n*k) is the number of observation in the sample set. Generally, Y..  is the best linear unbiased estimator of  Y.., where the measurements of sample are uncorrelated.  In a phantom experiment, Y..  can be replaced by a known physical measurement,  assuming that the known physical measurement converges to a population average.

- Variability: The tendency of the measurement process to produce slightly different measurements on the same test item, where conditions of measurement are either stable or vary over time, temperature, operators, etc. (http://www.itl.nist.gov/div898/handbook/index.htm).  The quantity defined as

where   is the mean of the data,   is number of observations in the sample set (http://www.itl.nist.gov/div898/handbook/eda/section3/eda356.htm).

For a changed measurement condition x, may be described as either “intra-x” or “inter-x” variability.  Namely, the variance equation as applied to measurements under changed conditions where x may be, for example, observer (reader), scanner, site, acquisition setting, etc.

Examples of variation in parameters for image analysis include time of day for scan; patient motion; patient hydration state; scanner hardware changes; scanner software changes; scan protocol errors; variability between patients, and other sources of variability.

  - Repeatability: Closeness of the agreement between the results of successive measurements of the same measurand carried out under the same conditions of measurement (http://physics.nist.gov/Pubs/guidelines/appd.1.html). (e.g., test-retest) (can apply on a phantom, vs. on a subject)

  - Reproducibility: Closeness of the agreement between the results of measurements of the same measurand carried out under changed conditions of measurement (http://physics.nist.gov/Pubs/guidelines/appd.1.html).

Given that in general we are estimating the variability under a limited set of observations, it becomes important to select the appropriate estimator which depends on the context.  As such, it is necessary to explicitly state the context, e.g., when it is appropriate to use more specific measures of this, including

- Coefficient of variation

- Mean of total variance

- Mean squared error

More complex models as indicated to partition the causes of variation among the factors present in any given experiment

  - Precision: Closeness of agreement between indications or measured quantity values obtained by replicate measurements on the same or similar objects under specified conditions (http://www.bipm.org/utils/common/documents/jcgm/JCGM_200_2008.pdf).

Defined in terms of aggregate variability (i.e., same equation as variance, but inclusive of all intra- and inter- variability for the manifest factors experienced in a real-world condition and expressed as number of significant digits accounting for that variance).

# General implementation of the challenge studies

The following outlines the procedure to be taken by participants:

- Submit an email to the trusted registrar (non-competing organization) with the signed  Participation Agreement and receive an anonymous ID back for identification of results.

- Download and read the 3A Challenge Protocol as posted to the 3A Wiki.

- Download the 3A Challenge data as described in the Protocol.  This data will be inclusive of a defined development (e.g., training) set for algorithm adjustment and a test set on which the results would be measured.  Data will include images and one location point per target lesion defined by a non-participant.

- Once the development set is used by the algorithm to do any parameter tuning, these tuning parameters should be used without further modification on the test set (similar to MICCAI liver challenge in 2008). (Note: individual participant integrity is relied on to enforce this policy.)

- Report your results in the required formats, signed by your team leader, to 3A registrar. (Note: this report has to include an method description also.)

- 3A registrar will analyze the reported results as per the Analysis section of this document. 3A registrar will provide Participants with individual analysis of their results. We will publish the results of the evaluation, without publicly identifying individual scores by Participant.

## Flow of events for each challenge study

In this case there are two primary actors: the participant, and the honest broker:

- Individual participant:

  - Method (including any algorithms used) included in the imaging test for data and results interpretation must be pre-specified before the study data is analyzed. Participants will be provided a development set for any algorithm tuning, such development set to be comparable to the test set, but without any repeated use of the same data. Lung data is very different from liver, for example. Alteration of the method to better fit the data is generally not acceptable and may invalidate a study.

  - The individual participant or organization needs to receive back performance data and supporting documentation capable of being incorporated into regulatory filings at its discretion.

- 3A registrar: needs means to archive data sets that may be selectively accessed according to specific clinical indications and that may be mapped to image quality standards that have been described as so-called “acceptable”, “target”, and “ideal”

- The development set will continued to be available but should be stable whereas test sets may be refreshed with new cases for direct access by interested investigators for testing of new imaging software algorithms or clinical hypotheses. Future investigators will have access to the development set and test sets for additional studies.

- Define services whereby the test set is indirectly accessible via the trusted broker (which means that training data will be accessible each time and only for the test data the user needs contact to the trusted broker).

## Results

Each participant has to be informed (only the anonymized group results with an indication of which member they are).  Likewise, the team will produce a publication of the results (to all participants), with authorship representing participants.

At this point, it is possible to apply the study infrastructure to new participants as desired, reporting as follows:

Figure 5: Radar plot showing the performance of a new method as compared to the group, where in this case the new method tends to perform poorly.

Figure 6: Radar plot showing the performance of a new method as compared to the group, where in this case the new method tends to perform quite well with respect to the group value. In such a case, the decision of the community may be to advance the group value to capture the improved state of the art, though in general it may not do so until or unless more than one supplier outperforms the prior group value so as to retain wide availability of compliant methods.

## Study Design

### Data

Reference Data Sets will be established and made available to participants, with designated purpose as a “Training” set or a “Test” set.  As indicated in Figure 1, an example use is that an challenge study proceeds with a Pilot phase performed using a subset of data, after which a Pivotal phase is run on additional data.  The initial Pilot phase includes data partially marked with truth and partially not.  The part marked with truth may be utilized for training or optimization purposes and the part not so marked shall be used for the pilot test results.  After all participants return their pilot results, the full truth markings are made available to the participants thereby creating a larger set that may be used for training and optimization prior to running the Pivotal.  The Pivotal set is referred to as the Test set, and full truth data is not shared until or unless the community determines that it will not be further used for pivotal testing, implying that the test set is refreshed with new data for subsequent pivotal testing.

### Location Coordinates and Ground Truth

Reference Data Sets will be accompanied by location points defined in the context of an indexing scheme.  The purpose of this is so as to achieve consistency across participants such that each lesion is identified in the same way.  Participants are allowed to select different or multiple seed point(s), provided they utilize the lesion identification scheme provided.

Truth is known absolutely in challenge study where phantoms are utilized for the absolute volume estimation study and external measurements are made.  Ground truth is also known in so-called “coffee break” change studies performed on scans separated by a short time period so as to establish that there is no actual biological change; hence truth is known to be zero.  In practice (and hence the point of the exercise) the measurements made will not be zero hence the interest of the study.

### Approach to Statistical Analysis of the Challenges

Statistical measures calculated in these studies include Uncertainty (specifically Bias) and Variability (specifically Variance).  Interestingly, we don’t include Accuracy among these, as the term is formally understood to be a qualitative one that reflects whether a result is “right” or “wrong” rather than a numeric quantity.  As such, we do estimate Bias, but reserve Accuracy for the clinical interpretation of these measurements rather than applying at the level of the measurements themselves.

Likewise, note that Precision and Reliability (comprised of Repeatability and Reproducibility) is not assessed in these studies.  The reason for this is we presently don’t include repeated measurements and/or use of alternative seed points.  It is possible to pursue extended studies that estimate these performance characteristics as well but the present scope precludes them.

#### Characterizing Performance of Absolute Volume Estimation where Ground Truth is Known

The following parameters are assessed in a study where ground truth is known (note that we refer to references measurements as being “ground truth” if the precision of the measurement used to establish the reference is orders of magnitude greater than the measurement method under study):

- Uncertainty

  - Bias: mean of measured volume minus the physical measurement of the anthropomorphic lesion object.  Expressed as percent of actual.

where    is the percent difference in volume (i.e. (measured –ground truth) /ground truth*100) in ith lesion and measured by jth method,    is the mean of the percent difference across lesions and methods, N (= n*k) is the number of observation in the sample set.    is set to zero based on the law of large number. Thus ias is the mean of the percent difference in volume.

- Variability

  - Variance: estimate overall variance in the difference of measured volume from known physical measure or in the difference of two calculated measured volumes in the same lesion in two images (e.g. different factor levels; slice thickness).

In this study, there are four factors to explain the measurement variability, which are shape, density, slice thickness, and participants.  The notation of factor can be set as (, (, (, and ( for shape, density, slice thickness, and participants, respectively. Yijklm can be the relative bias or the measurement for testing uncertainty or the volume measurement of software for testing variability.

For considering ANOVA with simple four factors without considering interaction,

Overall variance:

Variance due to shape:

Variance due to density:

Variance due to slice thickness:

Variance due to participants: ,

where and  , 	and , and ,

and  ,  	and .

In addition, the a, b, c, and d are the number of categories for shape, density, slice thickness, and participants, where n is the number of repeated measurement.

The above is assessed at two levels. First, the group of methods that collectively comprise the so-called acceptable assay methods for the biomarker. Second, the performance of individual methods, in terms of how the individual results compare with the dispersion evident in the group.

- Perform the participant methods on the reference data:

  - Analyze statistical variability across the following factors: 1. method type, 2. Image formation factors (exposure, pitch, collimation, slice thickness, reconstruction kernel), 3. Anthropomorphic factors (size, morphology, density, and attachment).

    - Overall: estimate bias and variance using mean, SD, box-plot (as a more flexible representation than Bland Altman) in the difference of measured volume from the ground truth

    - Similar analysis for each factor

    - (group discussion needed on whether degree of automation is in scope)

  - Additionally, perform  ANOVA or regression analysis to test the variability among methods and degree of automation utilized

  - Identify  outliers whose bias are greater than 30% and report a summary in characteristics of lesion

- Assess the performance of each descriptive statistic (in our case, Bias and Variance but more generally to include others such as Accuracy, Precision, Repeatability and Reproducibility) and describe them in a box plot similar to the following example:

Figure 2: Box plots showing dispersion of participant results for each of the descriptive statistics selected for the study.

- Select a “group value” for each of the descriptive statistics, e.g., as the mean plus 2 std.

- For each participant, report their results back to them in the following form:

Figure 3: Radar plot showing the “group value” and how one of the individual participant methods compares with it.

Figure 4: Radar plot showing the comparative performance among individual participant methods shown altogether.

The above is assessed at two levels. First, the group of test that collectively comprises the acceptable assay methods for the biomarker. Second, the performance of individual test, in terms of their membership.

- The following comparisons of markups can be made:

  - Analyze statistical variability across the following factors: 1. Method type, 2. Lesion features (size, morphology, measurable/measurable, attachment, contrast of boundary).

    - Overall: using mean, SD, box-plot using the difference of two time points where there is no biological differences in lesion

    - Similar analysis for each factor

  - Calculate the precision of the changes in estimated volumetric measures in thresholds of 5%, 10%, 15%, 20%, 25%, and 30%.

    - Overall: using mean, SD, graph of the precision (%) vs. the thresholds, water-fall plot

    - Similar analysis for each factor

  - Additionally, perform  ANOVA or regression analysis to test the variability among methods and degree of automations

  - Identify  outliers whose precision are greater than 30% and report a summary in characteristics of lesion

Subsequently, follow steps 2-4 as defined above using these descriptive statistics.

# Endpoints and Investigations

There are two progressions going on: one from Pilot to Pivotal, and the other, from Primary Investigations to Secondary Investigations.  The first derives from the thought that any step may be piloted. Any pilot we do is understood as merely being a miniature of the corresponding pivotal: not different in what’s done, only what cases (and the number of cases) we do it on.  As such, all steps (including plotting steps) would be done the same way in a pilot as it is on the pivotal. The second progression derives from a step-wise progression from (easier) to (more complex) investigations so that the community learns together over time (Fig. 1).

Fig. 1 Primary and secondary endpoints: for each challenge study, a Pilot phase is performed using a subset of data, after which a Pivotal phase is run on additional data.  The initial Pilot phase includes data partially marked with truth and partially not.  The part marked with truth may be utilized for training or optimization purposes and the part not so marked shall be used for the pilot test results.  After all participants return their pilot results, the full truth markings are made available to the participants thereby creating a larger set that may be used for training and optimization prior to running the Pivotal.  The Pivotal set is referred to as the Test set, and full truth data is not shared until or unless the community determines that it will not be further used for pivotal testing, implying that the test set is refreshed with new data for subsequent pivotal testing.

## Primary Investigations

Study objectives (in priority and sequence order):

- Characterize Performance of Absolute Volume Estimation where Ground Truth is Known: Results on phantom data, e.g., accuracy and variability, on scans of an anthropomorphic phantom (according to the work of the QIBA 1A Group. (see Dr. Petrick‘s paper, SPIE 2011).  Results on these data utilize the absolute volume primary endpoint.

- After an initial pilot study (1 above) we will proceed to Characterize Performance of Change Estimation in the Absence of Biological Change for results on clinical data, e.g., minimum detectable change and reproducibility.  The study will utilize the same data set as used in the 1B study.  Results on these data utilize the percent change in volume primary endpoint.

## Secondary investigations (future plans, needs study design extension in the future)

Extended study for additional measures of method effectiveness:

- MICCAI-like objective criteria of method performance

- Usability or workflow-effectiveness evaluations (e.g., how many corrections, how fast the algorithm ran (time), etc.

Extended study to explore trusted broker scenarios:

- Sequester data and have a black-box wrapped full automated algorithm produce results;

- Support impartial readers to use participant-defined interfaces to their methods (allowing whatever training they recommend beforehand but otherwise not have access to the raw imagery prior to the test).

These secondary investigations are expected to utilize the informatics infrastructure but are otherwise not being actively developed at this time.

Extended study to characterize performance of change estimation in the presence of biological change is generally understood to be out of scope for 3A at this time, covered in QIBA’s 3B effort.  This does not preclude use of the infrastructure for such studies, however, and in fact it is understood as desirable for this to be supported in the future.

## Primary and secondary endpoints

The primary endpoint depends on the study data utilized.  In such cases where there is a single time point per case, the primary endpoint is volume in mm3.  In such cases where there are two time points, the primary endpoint is percent change in volume from the first time point.

### First 3A challenge study: Absolute volume estimation

This part of the study utilizes a reference data set comprised of the similar cases as used in the 1A study but across all lesions present in those cases (as opposed to only one lesion per case as was the case for the 1A reader study).  It also extends the statistical analysis that was conducted for 1A in the manner defined above.

- Defined challenge: estimate absolute volumes in phantom data

  - Explicitly indicate experimental factors (primary: analysis sw model.  Secondary is acquisitions settings)

  - Explicitly indicate descriptive statistics: bias, variance

  - Null hypothesis: individual methods have bias and/or variance exceeding 15%. (alternative is that both bias and variance of any individual method is less than 15%) (we should probably do a more formal error propagation model, but this simple aggregate uncertainty statement will suffice for now.)

- Policy regarding test data: participants see test data but are asked not to use it in algorithm optimization.  Training data is available for any use to support their participation in the challenge that the participant desires (including not using it at all, for example, if they feel they have sufficient data on which their algorithm has been optimized).

- Defined set of data (cases drawn from the FDA CDRH data set):

  - All data associated with the challenge shall comply with the QIBA profile.

  - Pilot: for sandbox practice, and to be used in the power study for the pivotal:

    - Training: 5 cases, all lesions per case

    - Test: same 10 cases, all lesions

  - Pivotal: for published results:

    - Training: participants may use all of the 15 pilot cases for method optimization

    - Test: <number of cases/lesions as determined in the power study as derived based on the pilot> cases

#### Statistical Analysis of First 3A Challenge

<grace to fill in>

### Present thought on next 3A challenge study

- Defined challenge: estimate volume change

- Policy regarding test data:

- Defined set of data (cases same as was used in 1B):

  - Pilot

  - Pivotal

# Appendix: Factor Effects Model- full details

ANOVA full model for a four-factor study

m= number of case (m=1,2,…,nijkl  for unequal repeated measurements  or m=1,2,…,n for otherwise).

Shape:

Density:

Slice thickness:

Participants:

- Analysis of variance

Notation

Fitting of ANOVA Model

Parameter				Estimator

Partitioning of Total Sum of Squares

Degrees of Freedom and Mean squares

Table 23.2

| Source of Variation | SS | df | MS | E{MS} |
| --- | --- | --- | --- | --- |
| Factor A (shape) | SSA | a-1 | MSA |  |
| Factor B (density) | SSB | b-1 | MSB |  |
| Factor C (slice thickness) | SSC | c-1 | MSC |  |
| Factor D (participants) | SSD | d-1 | MSD |  |
| AB interactions | SSAB | (a-1)(b-1) | MSAB |  |
| AC interactions | SSAC | (a-1)(c-1) | MSAC |  |
| AD interactions | SSAD | (a-1)(d-1) | MSAD |  |
| BC interactions | SSBC | (b-1)(c-1) | MSBC |  |
| BD interactions | SSBD | (b-1)(d-1) | MSBD |  |
| CD interactions | SSCD | (c-1)(d-1) | MSCD |  |
| ABC interactions | SSABC | (a-1)(b-1)(c-1) | MSABC |  |
| ABD interactions | SSABD | (a-1)(b-1)(d-1) | MSABD |  |
| ACD interactions | SSACD | (a-1)(c-1)(d-1) | MSACD |  |
| BCD interactions | SSBCD | (b-1)(c-1)(d-1) | MSBCD |  |
| ABCD interactions | SSABCD | (a-1)(b-1)(c-1)(d-1) | MSABCD |  |
| Error | SSE | abcd(n-1) | MSE |  |
| Total | SSTO | abcdn-1 |  |  |

Test for Factor effects

all

not all equal 0

If , conclude

If , conclude

The rest of factors can be tested and the details are listed below.

Table 23.3

| Alternatives | Test Statistic | Percentile |
| --- | --- | --- |
| all not all |  |  |
| all not all |  |  |
| all not all |  |  |
| all not all |  |  |
| all not all |  |  |
| all not all |  |  |
| all not all |  |  |
| all not all |  |  |
| all not all |  |  |
| all not all |  |  |
| all not all |  |  |
| all not all |  |  |
| all not all |  |  |
| all not all |  |  |
| all not all |  |  |

all

not all equal 0

If , conclude

If , conclude

# References

# Footnotes

It should be noted that RECIST has not been shown to reliably achieve an accurate and precise measurement with a 20% SLD measurement.

For our purposes, since we are gaining experience with this concept, we arbitrarily consider the list of participants to comprise this group.  As we gain experience with this method and/or replace it with better ones, we will tighten how we define “acceptable methods” in line with the QIBA Profile specifications.

Deng X and Du G. 3D segmentation in the clinic: A grand challenge II – liver lesion segmentation 2008. http://lts08.bigr.nl

# Endnotes

Moertel CG, Hanley JA. The effect of measuring error on the results of therapeutic trials in advanced disease. Disease 1976; 38: 388-394.

Quivey JM, Castro JR, Chen GT, Moss A, Marks WM. Computerized tomography in the quantitative assessment of tumour response. Br J Disease Suppl 1980; 4:30-34.

Munzenrider JE, Pilepich M, Rene-Ferrero JB, Tchakarova I, Carter BL. Use of body scanner in radiotherapy treatment planning. Disease 1977; 40:170-179.

Petrou M, Quint LE, Nan B, Baker LH. Pulmonary nodule volumetric measurement variability as a function of CT slice thickness and nodule morphology. Am J Radiol 2007; 188:306-312.

Bogot NR, Kazerooni EA, Kelly AM, Quint LE, Desjardins B, Nan B. Interobserver and intraobserver variability in the assessment of pulmonary nodule size on CT using film and computer display methods. Acad Radiol 2005; 12:948–956.

Erasmus JJ, Gladish GW, Broemeling L, et al. Interobserver and intraobserver variability in measurement of non-small-cell carcinoma lung lesions: Implications for assessment of lesion response. J Clin Oncol 2003; 21:2574–2582.

Winer-Muram HT, Jennings SG, Meyer CA, et al. Effect of varying CT section width on volumetric measurement of lung lesions and application of compensatory equations. Radiology 2003; 229:184-194.

Buckler AJ, Mozley PD, Schwartz L, et al. Volumetric CT in lung disease: An example for the qualification of imaging as a biomarker. Acad Radiol 2010; 17:107-115.

Radiological Society of North America. http://qibawiki.rsna.org/index.php?title=Main_Page, accessed 07 Sep 2009.

http://www.grand-challenge.org/index.php/Main_Page, accessed 23 December 2010.

http://www.preventcancer.org/uploadedFiles/Education/Conferences,_Workshops,_and_Educational_Programs/Day-2-Friday-1100-AM-Tony-Reeves.pdf, accessed 23 December 2010.

http://www.nist.gov/itl/iad/dmg/biochangechallenge.cfm, accessed 23 December 2010.

Petrick NP, Kim HJ, Clunie D, Borradaile K, Ford R, Zeng R, Gavrieldes MA, McNitt-Gray MF, Fenimore C, Lu J, Zhao B, Buckler AJ. Evaluation of 1D, 2D and 3D nodule size estimation by radiologists for spherical and non-spherical nodules through CT thoracic phantom imaging, SPIE, February 2011.