Profile: FDG-PET/CT as an Imaging Biomarker Predicting Response to Cancer Therapy for Patient Management and Oncologic Drug Development

Version 0.3

5 March 2011

Table of Contents

I. Executive Summary	3

II. Clinical Context and Claims	3

Claim 1:  Response Assessment	3

III. Profile Details	4

0. Reserved (included above)	5

1. Reserved (relevance restricted to Protocol)	5

2. Reserved (relevance restricted to Protocol)	5

3. Subject Scheduling	5

4. Subject Preparation	5

5. Imaging-related Substance Preparation and Administration	5

6. Individual Subject Imaging-related Quality Control	8

7. Imaging Procedure	8

8. Image Post-processing	14

9. Image Analysis	15

10. Image Interpretation	20

11. Archival and Distribution of Data	21

12. Quality Control	24

13. Imaging-associated Risks and Risk Management	28

IV. Compliance	29

Acquisition Scanner	29

Contrast Inject Device	30

Analysis Software	30

Viewing System	30

Performing Site	30

References	30

Appendices	30

Appendix A: Acknowledgements and Attributions	30

Appendix B: Background Information	30

Appendix C: Conventions and Definitions	30

Appendix D: Documents included in the imaging protocol (e.g., CRFs)	31

Appendix E: Associated Documents	32

Appendix F: TBD	32

Appendix G: Model-specific Instructions and Parameters	32

# I. Executive Summary

This Profile documents specifications and requirements for the use of FDG-PET as an imaging biomarker in oncologic indications. It covers both clinical trial usage as well as individual patient management. The document is built in part from extracting relevant information from its sister UPICT protocol as indicated below as well as directly through the efforts of the QIBA FDG-PET Technical Subcommittee.

Summary of Clinical Trial Usage as described in assimilated protocol "**Title of the Imaging Protocol"

**Provide a brief (less than 250 words) synopsis to let readers quickly determine if this imaging protocol is relevant to them. Sketch key details such as the primary utility, imaging study design, specific aims, context, methods, expected results, risks, and deliverables.

# II. Clinical Context and Claims

The clinical context sets out the utilities and endpoints for clinical trial usage and then proceeds to identify targeted levels of accuracy for named measurement read-outs that may be used in the clinical trial setting and/or individual patient management.

Utilities and Endpoints for Clinical Trials

**Describe one or more utilities or endpoints this Imaging Protocol could serve in a Clinical Trial. (e.g. to determine eligibility of potential subjects in the clinical trial; to triage eligible subjects into cohorts based on stage or severity of disease; to assess response to treatment; to establish the presence of progression for determining TTP, PFS, etc.; to monitor for adverse events; to establish a database for the development, optimization, and validation of imaging biomarkers, etc.)

## Claim 1:  Response Assessment

FDG-PET scans are sensitive and specific for detection of malignant tumors. FDG-PET scans reliably reflect glucose metabolic activity of cancer cells and can be measured with high reproducibility over time. Longitudinal changes in tumor FDG activity during therapy predict clinical outcomes (define examples?) earlier than changes in standard anatomic measurements. Therefore, tumor response or progression as determined by tumor FDG activity will be able to serve as an endpoint in well-controlled Phase II and III efficacy studies of cytotoxic and targeted therapies in FDG-avid tumors. In tumor/drug settings where the preceeding phase II trials have shown a statistically significant relationship between FDG-PET response and an independent measure of outcome, changes in tumor FDG activity can then serve as the primary endpoint for regulatory drug approval in registration trials.

Profile specified for use with: , for the following indicated biology: , and to serve the following purpose: .

Compliance levels for results are given in the table below.

| Measurement or Categoric Result | Performance Levels Achieved under Bull's Eye Conditions |
| --- | --- |
| SUVmax | If Activities are Performed at Acceptable Level <1.0% If Activities are Performed at Target Level <0.1% If Activities are Performed at Ideal Level <0.01% |
| **for example, PR | If Activities are Performed at Acceptable Level **e.g., coef. of corrlelation 85% If Activities are Performed at Target Level **e.g., coef. of correlation 90% If Activities are Performed at Ideal Level **e.g., coef. of correlation 95% |
| **for example, presence of carcinoma | If Activities are Performed at Acceptable Level e.g., AUC of ROC 80% If Activities are Performed at Target Level e.g., AUC of ROC 87% If Activities are Performed at Ideal Level e.g., AUC of ROC 90% |

# III. Profile Details

The following figure provides a graphical depiction that describes the marker at a technical level.

The identified activities are described in the detail sections given below.

## 0. Reserved (included above)

## 1. Reserved (relevance restricted to Protocol)

## 2. Reserved (relevance restricted to Protocol)

## 3. Subject Scheduling

**Describe requirements and considerations for the physician when scheduling imaging and other activities, which may include things both related and unrelated to the trial.

## 4. Subject Preparation

**Describe how subjects are prepared.

## 5. Imaging-related Substance Preparation and Administration

**(e.g. Contrast agents, radiopharmaceuticals or stress agents intended to directly affect the imaging process. Does not include therapeutic drugs/agents unless they are also imaging agents.)

5.1. Substance Description and Purpose

**Describe the substance and its purpose, stating any requirements needed.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
| DICOM recording | Acceptable Substance description and purpose Target Ideal |

5.2. Dose Calculation and/or Schedule

**Describe the dosce calculation and/or schedule, placing any needed requirements.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
| DICOM recording | Acceptable Dose calculation and schedule Target Ideal |

5.3. Timing, Subject Activity Level, and Factors Relevant to Initiation of Image Data Acquisition

**Describe the timing, subject activity level, and factors relevant to initiation of image data acquisition. Place needed requirements.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
| DICOM recording | Acceptable Subject activity level Target Ideal |

5.4. Administration Route

**Describe the administration route, placing any needed requirements.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
| DICOM recording | Acceptable Administration route Target Ideal |

5.5. Rate, Delay and Related Parameters / Apparatus

**Describe the rate, delay, and related parameters or apparatus. Place needed requirements.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
| DICOM recording | Acceptable Rate and delay Target Ideal |

5.6. Required Visualization / Monitoring, if any

**Describe the required visualization or monitoring, placing any needed requirements.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

5.7. Quality Control

See 12.2

## 6. Individual Subject Imaging-related Quality Control

See 12.3

## 7. Imaging Procedure

This section describes needed specifications and requirements related to the actual imaging procedure. It is structured in such a way as to extract relevant content from the Protocol and then extending that with extensions necessary to explicitly meet the claims as set in the Profile.

**When the imaging procedure involves acquisition of multiple series, Section 7 may be repeated (7a, 7b) as necessary to describe each acquisition.

7.1. Required Characteristics of Resulting Data

**Describe the characteristics of the imaging data resulting from acquisition and reconstruction that are relevant to its use in the clinical trial. This description is generally independent of the vendor, platform, and version of the imaging equipment.

7.1.1. Data Content

**Describe what the acquired images should contain/cover. (e.g. Anatomic Coverage, Field of View)

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
| Scan duration per bed position | Acceptable Target Ideal |
| Number of bed positions | Acceptable Target Ideal |

7.1.2. Data Structure

**Describe how the data should be organized/sampled. (e.g. Spatial Resolution, Collimation Width, Slice Interval, Temporal Resolution)

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

7.1.3. Data Quality

**Describe any needed measurements of quality. (e.g. Image Quality, Noise Levels, Motion Artifacts, Radiation Dose)

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

7.2. Imaging Data Acquisition

The following sections describe the acquistion of imaging data.

7.2.1. Subject Positioning

**Introduce the section.

**Describe the subject positioning and place needed requirements.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

7.2.2. Instructions to Subject During Acquisition

**Introduce the section.

**(e.g., breath hold, etc.)

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

7.2.3. Timing/Triggers

**Introduce the section.

**(e.g., relative to administration of imaging agents; inter-time point standardization)

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

7.2.4. Model-specific Parameters

Appendix G.1 lists acquisition parameter values for specific models/versions that can be expected to produce data meeting the requirements of Section 7.1.

7.2.5. Archival Requirements for Primary Source Imaging Data

See 11.3

7.2.6. Quality Control

See 12.3

7.3. Imaging Data Reconstruction

**Introduce the section.

**Describe the data reconstruction process including any inherent data correction, smoothing, etc. This may conceivably be performed on a different system than acquisition, and occasionally at a later time, particular for supplementary reconstructions.

7.3.1. Input Data to Be Used

**Introduce the section.

**Place requirements on the input data to be used.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

Parameters that need to be available for the user to be specified (and stored in a study specific acquisition/reconstruction protocol) are:

| Parameter | Compliance Levels |
| --- | --- |
| Image matrix size | Acceptable (128-512), zoom (1-2) OR voxel size (2,3,4,5 mm). Should be reconstructed voxel size and not obtained after rebinning of reconstructed image) Target Ideal |
| Number of iterations and subsets (and relaxation factor) | Acceptable Target Ideal |
| ToF kernel size | Acceptable Target Ideal |
| Image filtering (type and FWHM) | Acceptable Target Ideal |

7.3.2. Methods to Be Used

**Place requirements on the methods to be used.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

Data can be reconstructed including all corrections needed for quantification as well as without scatter and attenuation correction. Iterative reconstruction method should be applied.   PET/CT systems are equipped with a harmonized reconstruction protocol (NB not the algorithm or settings are harmonized, but the resulting specified quantitative image characteristics for specified phantoms/experiments) – SNM Image Reconstruction Workgroup.

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

7.3.3. Required Characteristics of Resulting Data

**Place requirements on characteristics of resulting data.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

Store PET image data always in units of Bq/ml in DICOM files, decay reference time should equal (PET) scan acquisition time and integral model should be used for decay correction.

Vendors should clearly specify which time (series, study, acquisition, dose essay time, injection time) is used as reference for decay correction when data are given in units Bq/ml.

All needed information for fully corrected net injected activity (e.g. residual activity, injection time, calibration time) is required. Scanner performs all decay corrections (not the operator)

The matrix, slice thickness, and reconstruction zoom will yield a target voxel size of 3 – 4 mm in all three dimensions, although not necessarily isotropic and not achieved by rebinning etc of the reconstructed images

Include reference tissue value (e.g. 3 cm diameter VOI in liver)

Mechanism for flagging artifacts (motion, extravasation, etc.)

decay reference time should equal (PET) scan acquisition time and integral model should be used for decay correction

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

7.3.4. Platform-specific Instructions

Appendix G.2 lists reconstruction parameter values for specific models/versions that can be expected to produce data meeting the requirements of Section 7.2.

7.3.5. Archival Requirements for Reconstructed Imaging Data

See 11.4

7.3.6. Quality Control

See 12.4

## 8. Image Post-processing

**Describe subsequent modification of the reconstructed image pixels prior to analysis. This is often performed on a different platform than the acquisition system. (e.g. spatial registration, spatial re-orientation, re-slicing, feature enhancement, 3D view generation)

8.1. Input Data to Be Used

**Describe required input data and any necessary validation or adjustments which should be performed on it. (e.g. particular image series or views; raw, processed, both)

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

8.2. Methods to Be Used

**Describe how the analysis should be performed. (e.g. algorithms to be used; where measurements should be taken; definition of key anatomical points or pathology boundaries; related annotations)

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

8.3. Required Characteristics of Resulting Data

**Place requirements on characteristics of resulting data.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

8.4. Platform-specific Instructions

Appendix G.3 lists post-processing parameter values for specific models/versions that can be expected to produce data meeting the requirements of Section 8.

8.5. Archival Requirements

See 11.5

8.6. Quality Control

See 12.5

## 9. Image Analysis

Obtain actual maximum activity concentration or voxel value (units Bq/ml) and maximum SUV (BW, LBM, BSA normalised), which are the activity concentration value and the SUV of a single voxel from the actual original image that has the highest value within a volume of interest drawn around the object of interest. The latter will avoid additional error in activity concentration values and SUVmax due to viewing/display interpolation and/or minimize round-off errors in SUV calculation within defined tolerances.

**Describe the generation of new data/information based on the images. This may be performed by an automated program, a semi-automated program, or entirely by a human. (e.g. organ segmentation, size or volume measurement, flow rate calculation, tissue characterization, observation of the presence/absence/degree of features such as edema)

9.1. Input Data to Be Used

**Describe required input data and any necessary validation or adjustments which should be performed on it. (e.g. particular image series or views; raw, processed, both)

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

DICOM image set from patient PET scan.

Necessary metadata that is not captured by the PET scanner acquisition process. This may include for example, post-injection residual dose or parameters needed for lean-body-mass SUV normalization.

Covariates:

Weight - allow disabling of auto weight import from HIS/RIS  Height - required field

All needed information for fully corrected net injected activity (e.g. residual activity, injection time, calibration time) is required. Scanner performs all decay corrections (not the operator)

Blood glucose (from CLIA compliant device) at time of injection is recorded with DICOM patient information  All scanner times and/or all clocks in a PET/CT system should be synchronized to NTP

Patient meta-data recorded, e.g. using enhanced DICOM attributes

Displays should have ability to show information that effects SUVs (uptake time, etc.)

Tumor ROI's reflecting the metabolic volume of the tumor is desirable. Volumes based on a 50% and (?) 70% threshold of the peak tumor SUV should be produced. Alternative is to use the PERCIST threshold at 2SD above mean liver activity as a floor value for the ROI's. (?) These can reflect tumor volume and tumor volume x mean SUV lean - viewed as exploratory.

Measurement system (viewing and analysis software) shall provide the actual maximum voxel value in Bq/ml and the actual maximum SUV (SUVmax), which is the value or SUV of a single voxel from the actual original image (digital reference object, DRO) that has the highest value within a volume of interest drawn around the object of interest (maximum voxel value test object in DRO).

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
| ROI extraction of activity concentration | Acceptable <1.0% error Target <0.1% error Ideal <.01% error |

9.2. Methods to Be Used

**Describe how the analysis should be performed. (e.g. algorithms to be used; where measurements should be taken; definition of key anatomical points or pathology boundaries; scoring scales and criteria, related annotations)

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

9.2.1 ROI/VOI

The measurement system (viewing, ROI/VOI or analysis tool) is used by the user to define a 3D volume of interest around the SUVmax test object in the digital reference object (DRO). The VOI should fully encompass the entire test object in the DRO in all 3 directions by at least 2 voxel dimensions or 1 cm. ROI/VOI and analysis software is responsible for correct implementation of SUVmax extraction and calculation. The manufacturer should guarantee that maximum voxel value and/or SUVmax represents the activity concentration of a single voxel having the highest value within a 3D VOI. Moreover the manufacturer is responsible for correct implementation of SUV calculations, with e.g. correct implementation of corrections for decay. Moreover, the manufacturer should implement various versions of SUV normalizations (body weight, body surface area and lean body mass). Finally the manufacturer should guarantee that the same methodologies for obtaining the maximum voxel value (Bq/ml) and SUVmax from the DRO are available and can be applied to clinical whole body data.

9.2.2 Calculation of SUV

The VOI is used to extract the maximum voxel value (Bq/ml) and maximum SUV.

SUVmax normalized by body weight should be calculated as follows:

……………………………………………………………………………………………………….

SUVmax normalized by body surface area should be calculated as follows:

……………………………………………………………………………………………………….

SUVmax normalized by lean body mass should be calculated as follows:

……………………………………………………………………………………………………….

Report actual max. voxel value

Capablity to label, save, recall (in a std format, e,g, Advanced Technology Consortium (ATC) for Clinical Trials Quality Assurance)

Report VOI activity as Bq/ml

Report SUVs normalized to Weight, LBM, BSA

Report volume in cc (or ml) and voxels

Describe voxel inclusion policy

Use weighting for partial voxels

Fully included voxels use weight of 1.0

Output statistics inlcude mean, max, std. dev. to 3 sig figs

Describe rounding policy for outputs

VOI dimensions (sphere) should be specifiable to ±1 mm

Automatic centering for peak VOI calculation

Three threshold methods: fixed, % of max, gradient

Produce correct SUVs from QIBA DRO

All needed information for fully corrected nett injected activity (e.g. residual activity, injection time, calibration time) is required.

Scanner performs all decay corrections (not the operator)

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
| Activity concentration | Acceptable Target Ideal |
| Glucose correction | Acceptable Target Ideal |

9.3. Required Characteristics of Resulting Data

**Place requirements on characteristics of resulting data.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
| Method to compute maximum SUV ("SUVmax") | Acceptable SUV normalized by body weight Target Ideal lean body mass |
| Voxel value and/or activity concentration tolerances | Acceptable <1.0% up to 2 decimals Target <0.1% up to 2 decimals Ideal <.01% up to 2 decimals |
| SUVmax tolerance | Acceptable <1.0% up to 2 decimals Target <0.1% up to 2 decimals Ideal <.01% up to 2 decimals |

9.4. Platform-specific Instructions

Appendix G.4 lists image analysis parameter values for specific models/versions that can be expected to produce data meeting the requirements of Section 9.

9.5. Archival Requirements

See 11.6

9.6. Quality Control

See 12.6

## 10. Image Interpretation

**Describe the diagnostic conclusions of interest to be drawn from the images. (e.g. progression of disease, presence/absence/degree of pathology, viable tumor vs. necrotic)

**While Analysis is primarily about computation; Interpretation is primarily about judgment. Interpretation may be performed at both the lesional / target level and in the aggregate at the subject level (e.g., in an oncology study each index lesion may be measured in longest diameter during the analysis phase, but in this phase a judgment may be made as to whether there is a new “non-index” lesion; the aggregation of the measured lesions with comparison to previous studies coupled with the judgment as to the presence or absence of a new lesion will result in the RECIST classification at the subject level).

10.1. Input Data to Be Used

**Describe required input data and any necessary validation or adjustments which should be performed on it. May also specify data which should not be used until after the clinical trial interpretation is recorded. (e.g. particular image series or views; before and after processing versions of images to evaluate/validate the effects of processing; analysis results)

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

10.2. Methods to Be Used

**Describe how the interpretation should be performed. (e.g. definition of key anatomical points or pathology boundaries; scoring scales and criteria such as BIRADS, interpretation schema such as RECIST, related annotations)

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

10.3. Required Characteristics of Resulting Data

**Place requirements on characteristics of resulting data.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

10.4. Platform-specific Instructions

Appendix G.5 lists image interpretation parameter values for specific models/versions that can be expected to produce data meeting the requirements of Section 9.

10.5. Archival Requirements

See 11.7

10.6. Quality Control

See 12.7

## 11. Archival and Distribution of Data

**Introduce the section.

**Describe the required data formats, transmission methods, acceptable media, retention periods, … (e.g. Is the site required to keep local copies in addition to transmitting to the trial repository? Must all intermediate data be archived, or just final results? At what point may various data be discarded?)

11.1. Reserved

11.2. Reserved

11.3. Primary Source Imaging Data

The following requirements are placed on primary source imaging data.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

11.4. Reconstructed Imaging Data

The following requirements are placed on reconstructed data.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
| CT | Acceptable Target Daily water equivalent phantom values tracked in DICOM header Ideal |
| PET | Acceptable Daily/weekly/monthly scanner QA values included in DICOM header Target Daily uniform cylinder analysis, with link to results in patient DICOM header Ideal |
| Dose calibrator | Acceptable calibrated for F-18 using NIST-traceable source with information included in patient DICOM header Target Ideal |

11.5. Post-Processed Data

The following requirements are placed on post-processed data.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

11.6. Analysis Results

The following requirements are placed on analysis results.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

11.7. Interpretation Results

The following requirements are placed on interpretation results.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

## 12. Quality Control

**This is the section where all aspects of Quality Control are identified and described.

12.1. QC Associated with the Site

The following sectins consider various aspects of quality control.

12.1.1. Quality Control Procedures

**Describe required procedures and documentation for routine and periodic QC for the site and various pieces of equipment.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

Easy and fast procedure to adjust calibration of scanner, eg when dose calibrator is recalibrated then it would be very convenient to simply adjust calibration of scanner with a simple correction factor rather than an extensive procedure. Preferably a correction factor that is automatically generated and applied (upon user request) based on a calibration QC experiment.

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

12.1.2. Reserved

12.1.3. Reserved

12.2. QC Associated with Imaging-related Substance Preparation and Administration

The following requirements are placed on QC associated with imaging-related substance preparation and administration.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

12.3. QC Associated with Individual Subject Imaging

**fill in

The following sections describe aspects of QC associated with individual subject imaging.

12.3.1. Phantom Imaging and/or Calibration

**fill in

The following requirements are placed on phantom imaging and/or calibration.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

12.3.2. Quality Control of the Subject Image and Image Data

The following requirements are placed on QC of the subject image and image data.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

12.4. QC Associated with Image Reconstruction

The following requirements are placed on QC associated with image reconstruction.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

12.5. QC Associated with Image Processing

The following requirements are placed on QC associated with image processing.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

12.6. QC Associated with Image Analysis

The following requirements are placed on QC associated with image analysis.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

12.7. QC Associated with Interpretation

The following requirements are placed on QC associated with interpretation.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

## 13. Imaging-associated Risks and Risk Management

**Introduce the section.

The following sections consider various imaging-associated risks and risk management.

13.1. Radiation Dose and Safety Considerations

**Introduce the section.

The following requirements are placed regarding radiation dose and safety considerations.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

13.2. Imaging Agent Dose and Safety Considerations

**Introduce the section.

The following requirements are placed regarding imaging agent dose and safety considerations.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

13.3. Imaging Hardware-specific Safety Considerations

**Introduce the section.

The following requirements are placed regarding hardware-specific safety considerations.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

The following set of requirements extends what has been stated in the protocol.

| Parameter | Compliance Levels |
| --- | --- |
|  | Acceptable Target Ideal |

13.4. Reserved

13.5. Reserved

# IV. Compliance

## Acquisition Scanner

What we do to test for compliance by acquisitions systems

Use enhanced DICOM attributes to follow version number of software for: 1 Acquisition, 2 Reconstruction, 3 post-processing, 4 Display/VOI analysis, 5 Dynamic Analysis. Build list (on console) of dates of all s/w versions

## Contrast Inject Device

A power injector is required for DCE-MRI studies. It needs to be properly serviced and calibrated.

## Analysis Software

Analysis software, which performs SUVmax analysis. May be coupled to the PET/CT scanner system or provided by a 3rd party vendor.

[this is where we talk about compliance testing with a DRO]

[output parameters relative to a DRO have to be within tolerances specified in the details section above]

Users should use the DRO in order to verify correct implementation of maximum voxel value extraction and SUVmax calculations.

## Viewing System

**fill in

## Performing Site

Healthcare system (e.g. hospital or clinic)  including technologists and physicians, which both produce the PET DICOM images, perform the SUVmax analysis using analysis software, and analyze the results.

# References

**fill in

# Appendices

## Appendix A: Acknowledgements and Attributions

**

## Appendix B: Background Information

**

## Appendix C: Conventions and Definitions

Definitions: Review this document and define relevant terms and notations here.

Acquisition vs. Analysis vs. Interpretation: This document organizes acquisition, reconstruction, post-processing, analysis and interpretation as steps in a pipeline that transforms data to information to knowledge. Acquisition, reconstruction and post-processing are considered to address the collection and structuring of new data from the subject. Analysis is primarily considered to be computational steps that transform the data into information, extracting important values. Interpretation is primarily considered to be judgment that transforms the information into knowledge. (The transformation of knowledge into wisdom is beyond the scope of this document.)

Bulls-eye Compliance Levels Acquisition parameter values and some other requirements in this protocol are specified using a “bullseye” approach. Three rings are considered from widest to narrowest with the following semantics:

ACCEPTABLE: failing to meet this specification will result in data that is likely unacceptable for the intended use of this protocol.

TARGET: meeting this specification is considered to be achievable with reasonable effort and equipment and is expected to provide better results than meeting the ACCEPTABLE specification.

IDEAL: meeting this specification may require unusual effort or equipment, but is expected to provide better results than meeting the TARGET.

An ACCEPTABLE value will always be provided for each parameter. When there is no reason to expect better results (e.g. in terms of higher image quality, greater consistency, lower dose, etc.), TARGET and IDEAL values are not provided.

Some protocols may need sites that perform at higher compliance levels do so consistently, so sites may be requested to declare their “level of compliance”. If a site declares they will operate at the TARGET level, they must achieve the TARGET specification whenever it is provided and the ACCEPTABLE specification when a TARGET specification is not provided. Similarly, if they declare IDEAL, they must achieve the IDEAL specification whenever it is provided, the TARGET specification where no IDEAL level is specified, and the ACCEPTABLE level for the rest.

## Appendix D: Documents included in the imaging protocol (e.g., CRFs)

**(Material the site needs to submit)

**Subject preparation

**Imaging agent dose calculation

**Imaging agent

**Image data acquisition

**Inherent image data reconstruction / processing

**Image analysis

**Interpretation

**Site selection and Quality Control

**Phantom Imaging and Calibration

## Appendix E: Associated Documents

**e.g. the Imaging Charter, Site Manual, Standard Operating Procedures, etc.

## Appendix F: TBD

## Appendix G: Model-specific Instructions and Parameters

The presence of specific product models/versions in the following tables should not be taken to imply that those products are fully compliant with the QIBA Profile. Compliance with a profile involves meeting a variety of requirements of which operating by these parameters is just one. To determine if a product (and a specific model/version of that product) is compliant, please refer to the QIBA Conformance Document for that product. G.1. Image Acquisition Parameters The following technique tables list acquisition parameter values for specific models/versions that can be expected to produce data meeting the requirements of Section 7.1.

These technique tables may have been prepared by the submitter of this imaging protocol document, the clinical trial organizer, the vendor of the equipment, and/or some other source. (Consequently, a given model/version may appear in more than one table.) The source is listed at the top of each table.

Sites using models listed here are encouraged to consider using these parameters for both simplicity and consistency. Sites using models not listed here may be able to devise their own acquisition parameters that result in data meeting the requirements of Section 7.1 and conform to the considerations in Section 13.

In some cases, parameter sets may be available as an electronic file for direct implementation on the imaging platform.

# Text boxes

**target subpopulation

**biology

**biomarker use