## Slide 1
The Quantitative Imaging Biomarkers Alliance (QIBA®)
Edward F. Jackson, PhD – Chair, QIBA
Professor and Chair, Department of Medical Physics
University of Wisconsin School of Medicine & Public Health
July 22, 2016
Part I

## Slide 2: Quantitative Imaging Biomarkers
Biomarkers are characteristics that are objectively measured and evaluated as an indicator of normal biologic processes, pathogenic processes, or pharmacologic responses to a therapeutic intervention.1
Quantitative imaging biomarkers (QIBs) are objective characteristics derived from in vivo images as indicators of normal biological processes, pathogenic processes, or response to a therapeutic intervention.2
1NIH Biomarkers Definitions Working Group, Clin Pharmacol Therap 69(3):89-95, 2001
2Sullivan et al., Radiology 277(3):813-825, 2015 (www.rsna.org/qiba)

## Slide 3: Example MR QIB Applications
Existing MR QIBs:
  From simple morphological to numerous functional measures
T2
T2FLAIR
T1+Gd
Ktrans
kep
vp
ve
rCBV
rCBF
DWI
ADC
BOLD fMRI
ASL CBF
DTI FA

## Slide 4: Consumer Expectations for Quantification
94% of oncologists expect some or all tumors to be measured at the time of standard initial clinical imaging. (Jaffe T, AJR 2010)
Neurologists and psychiatrists desire quantitative measures of brain disorders (IOM Workshop, August 2013).
Pulmonologists desire CT-derived quantitative measures in COPD and asthma patients. (ATS/ERS Policy statement, Am J Resp Crit Care Med 2010)
Hepatologists desire quantitative measures of liver fat infiltration (Fitzpatrick E, World J Gastro 2014)
Rheumatologists desire quantitative measures of joint disease (Chu C, JBJS:J Bone Joint Surg 2014)
U.S. regulatory agencies (e.g., FDA) desire more objectivity in imaging scan interpretations.
Source: Daniel C. Sullivan, MD
Notes: ATS: American Thoracic Society
ERS: European Respiratory Society

## Slide 5: QIBs in Precision Medicine
Buckler, et al., A Collaborative Enterprise for Multi-Stakeholder Participation in the Advancement of Quantitative Imaging, Radiology 258:906-914, 2011

## Slide 6: Quantitative Imaging
In addition:
  Evidence-based medicine and QA programs depend on objective data
  Decision-support tools need quantitative inputs
  Radiomics and radiogenomics studies require quantitative data
P. Lambin et al. Eur J Cancer 48:441-446 2012

## Slide 7: QIB Challenges
Diagnostic Imaging Equipment ≠ Measurement Device
Measurement Device:
  Specific measurand(s) with known bias and variance (confidence intervals)
  Specific requirements for reproducible quantitative results
  Example: a pulse oximeter
Diagnostic Imaging Equipment:
  Historically: best image quality in shortest time (qualitative)
  No specific requirements for reproducible quantitative results (with few exceptions)

## Slide 8: QIB Challenges
General QIB challenges:
  Lack of detailed assessment of sources of bias and variance
  Lack of standards (acquisition, analysis, and reporting)
  Highly variable quality control procedures
    QC programs / phantoms, if any, typically not specific for quantitative imaging
  Little support (historically) from imaging equipment vendors
    No documented competitive advantage of QIB (regulatory or payer)
All lead to varying measurement results across vendors, centers, and/or time

## Slide 9: QIB Challenges
General QIB challenges:
  Cost of QIB studies (comparative effectiveness) / reimbursement
  Resource availability
    Technologists are not trained in advanced, quantitative, protocols
    Potential shortage of imaging scientists, data processing capabilities, etc.
  Radiologist acceptance
    QIBs are not part of radiologist education & training
    Lack of guidelines for QIB reporting
    Software and workstations needed to calculate and interpret QIB measures are not integrated into the radiologist’s workflow
    Clinical demand on radiologists is high --- “time is money”

## Slide 10: QIB Challenges
QIB Implementation and Qualification
  Data acquisition => Need for physical phantoms
    Application specific (potentially including human subjects)
  Data analysis => Need for synthetic phantoms
    “Digital reference objects” or DROs
    Application specific and, ideally, anthropomorphic
  Qualification => Need for clinical trials

## Slide 11: PET Reconstruction Harmonization
Source: Paul Kinahan, PhD
University of Washington
Sample of reconstruction settings from 68 academic centers
Vendor A
Vendor B
Vendor C
Harmonized results
Diameter (mm)
RC
Vendor A
Vendor C
Vendor B
Range of biases as a function of object size (1.0 is no bias) for different reconstruction settings
RC = Ratio of Observed Activity Concentration to Actual Activity Concentration
RC
Diameter (mm)

## Slide 12: Poor Reproducibility has Clinical Implications
Willemink MJ, et al. Coronary artery calcification scoring with state-of-the-art CT scanners from different vendors has substantial effect on risk classification. Radiology 173:695-702, 2014
  “Among individuals at intermediate cardiovascular risk, state-of the-art CT scanners made by different vendors produced substantially different Agatston scores, which can result in reclassification of patients to the high- or low-risk categories in up to 6.5% of cases.”
Oberoi S, et al. Reproducibility of noncalcified coronary artery plaque burden quantification from coronary CT angiography across different image analysis platforms. AJR Am J Roentgenol 202:W43-9, 2014
  “Currently available noncalcified plaque quantification software provides …poor interplatform reproducibility. Serial or comparative assessments require evaluation using the same software. Industry standards should be developed to enable reproducible assessments across manufacturers.”
Source: Daniel C. Sullivan, MD

## Slide 13: Adopting Metrology Principles in Imaging
Sources of bias and variance in QIB measurands are identified and mitigated to the degree possible.
  Bias* (accuracy):
    Often difficult to assess due to absence of reference standard (“ground truth”) measures
    Need application-specific phantoms
  Precision* (variance):
    Repeatability* – All conditions the same except short time separation (“test/retest”)
    – Repeatability coefficient
    Reproducibility* – Different operators, different days, etc.
    – Reproducibility coefficient
*Kessler, Barnhart, et al., Stat Meth Med Res 24:9-26, 2015; Sullivan, Obuchowski, et al. Radiology 277:813-825, 2016
available at www.rsna.org/qiba

## Slide 14: Adopting Metrology Principles in Imaging
Number of patients:
10% 12
20% 35
30% 78
40% 133
Levels of bias and variance remaining after mitigation are characterized => confidence intervals.
Knowing these levels translates to statistically valid study designs with adequate power and the fewest number of patients.

## Slide 15: RSNA QIBA
QIBA was initiated in 2007 under the leadership of Dan Sullivan
RSNA Perspective: One approach to reducing variability in radiology is to extract objective, quantitative results from imaging studies.
QIBA Mission
  Improve the value and practicality of quantitative imaging biomarkers by reducing variability across devices, patients, and time.
  “Industrialize imaging biomarkers”

## Slide 16: Qualitative Imaging => Biomarker Assays
Assays are characterized by their:
Technical Performance
  Clinical Performance
    Clinical validation
    Clinical utility

## Slide 17: RSNA QIBA Approach
Buckler, et al., A Collaborative Enterprise for Multi-Stakeholder Participation in the Advancement of Quantitative Imaging, Radiology 258:906-914, 2011
Select a Biomarker
Coordinate Groundwork
Draft QIBA Profile
Validate Equipment & Sites
Academic Use
Clinical Trial Use
Clinical Practice Use
- Transformational: addresses gaps, impacts public health
- Translational: concept proved, ready to advance
- Feasible: good change to succeed in near term
- Practical: leverages existing resources and technology
- Collaborative: engages HW/SW/agent stakeholders
- Identify significant sources of bias and variance
- Estimate achievable accuracy and precision
- Validate underlying assumptions and mechanisms
- Determine details to specify in the Profile
- Define claim (cross-sectional and/or longitudinal) and clinical context
- Specify details necessary for robust implementation
- Make details clear, implementable, and testable
- Define conformance criteria for each “actor” in imaging chain
- Test conformance with QIBA Profile specifications
- Publish validated products and sites